## Slide 1
ME2 VCM — Voice Controlled Smart Device
Always-on keyword + intent recognition at the edge · no cloud round-trip
15 October 2026 · El Veena Grace Rosero · Model · Dataset · Training on Apple MPS · Validation on RPi 4
Model
Mic · 16kHz → wake CNN → log-mel 40×96
DS-CNN trunk → BiGRU(128) · 0.367 M
Intent head · 20
Slot (fine) head · 37
Dispatcher → Actuator
Raspberry Pi 4 (4gb)
Item | Value
Parameters / weights | 0.367 M · ~1.6 MB ONNX (CRNN)
Compute | 62.78 M FLOPs / inference
+ wake gate | 0.249 M-param CNN · 1.0 MB (“Hello Jarvis”)
Validation on the Raspberry Pi 4
Item | Value
Wake / intent acc | 100 % wake (5,000 clips) / 91.6 % intent (test) · 88.6 % holdout
False-accept rate | 0.13 % wake FAR · 26.1 % FAR_oos @ min_conf 0.25
Latency p95 / RTF | 9.36 ms classify · 4.85 ms wake (on-Pi) / RTF 0.006
Live sessions | 247 wakes · 94 % recognized · 63 % acted ok · Oct 16 gate: 9/10 fired · 1 false fires
Runtime | onnxruntime (CPU) · 2 threads
Dataset
Item | Value
Source | HF airimonda/ai231-me2-voice-commands + supplementals (6 sources merged)
Hours / utts | 21.0 h / 36,604 clips: 29,836 train (17.3 h) · 6,305 test · 463 holdout
Speakers | 664 (speaker-disjoint splits)
Labels | 20 intents · 37 fine (slot) labels · OOS class
Training on Apple MPS (local Mac)
Item | Value
Hardware | Apple M-series · torch MPS backend
Objective | CE(fine) + 0.5·CE(intent) · label smoothing 0.05
Optimiser | AdamW wd 1e-4 · lr 1e-3 cosine · batch 128
Steps / loss | 60 epochs · seed 42 / 0.65 ~2.5 h wall-clock
Input | 16 kHz → log-mel 40×96 · z-scored · energy-norm
p. 1 / 2

## Slide 2
To Be Submitted
What the reviewer will look for
# | Item | Status
1 | Repo public, one-command reproduction | ✓ setup.sh + run.sh — verified on the Pi
2 | Dataset licensed and citable (DOI) | ✓ HF dataset → citable DOI: 10.57967/hf/10723
3 | Training logs + final checkpoint committed | ✓ train_crnn.jsonl · crnn.pt · onnx/
4 | Pi 4 latency reproduced by the posted script | ✓ perf.py bench/wake · p95 9.36 ms VCM · 4.85 ms wake (100+100)
5 | Held-out test set, unseen speakers | ✓ test 6,305 + holdout 463, speaker-disjoint
6 | Baseline of comparable size compared | single deployed model (CRNN 0.367 M); no baseline trained yet
Links & artefacts
Artefact | Where
GitHub repository | https://github.com/vrosero/AI231_MEx — public, MIT
Dataset location | huggingface.co/datasets/airimonda/ai231-me2-voice-commands
Training hardware | Apple M-series MPS (local Mac) · 60 epochs · seed 42
Model weights | crnn.pt + crnn.onnx (~1.6 MB) · jarvis_cnn.onnx (1.0 MB)
Demo: say “Hello Jarvis” → Jarvis responds “Yes” → say command → action
p. 2 / 2